## Slide 1: Wireless Networks and MOBILE Computing
BY Mr. VALENS NSENGIYUMVA
Communication Systems Engineer, Sweden
Telephone: 0787288628
Email: nvalens18@gmail.com

## Slide 2: 28. Diversity
Diversity is the use of multiple channels to increase the signal to noise ratio in the presence of random fading losses.
The idea of diversity is “don’t put all of your eggs in one basket”.
For fading channel there is a finite probability that a signal power will fall below any given fade margin.
There are several physical means to achieve multipath channels, and to get those channel nearly independent. Each has its advantages and disadvantages.

## Slide 3: Space diversity
Space diversity at receiver is the use of multiple antennas across space. Because multipath fading changes quickly over space, the signal amplitude received on the different antennas can have a low correlation coefficient.
In general we either accept that the correlation coefficient is not perfectly zero for 𝜆/2, or we separate the antennas further than 𝜆/2.
The problem with space diversity are most importantly that for consumer radios, we want them to be small ; and multiple antennas means that the device will be larger. This is fine when space is not a big concern for base stations.

## Slide 4: Space diversity
Another problem is in general a receiver with multiple antennas must have on RF chain(downconverter, LNA, filter) per antenna.
The benefits of space diversity are that no additional signal needs to be transmitted and no bandwidth is required.
MIMO is a kind of space diversity and multipath diversity.

## Slide 5: Polarization diversity
Polarization diversity is the use of two antennas with different polarizations. (horizontal and vertical)
The advantages of polarization diversity is that two antennas don’t need to be spaced apart, so polarization diversity can possibly be done on mobile device.
It may be combined with space diversity so to further reduce the correlation coefficient between received at two antennas.
Polarization diversity, like space diversity doesn’t require any additional bandwidth or signal transmission from the transmission from the transmitter.
The disadvantages are simply that there can be only two channels -vertical and horizontal polarizations. It may require two receiver RF chains.

## Slide 6: Frequency diversity
Frequency diversity uses multiple transmission on different center frequencies. This doesn’t typically means transmitting exactly the same thing on multiple bands(which would require multiple times more bandwidth). E.g. OFDM
Advantages of frequency diversity are that only one antenna, and one RF chain, is needed.
A disadvantage is that, because some of the transmit power is used to send data in bands that are in deep fades, the power efficiency is less compared to space diversity, in which the transmitter sends all of its power in one channel.

## Slide 7: Multipath diversity
Multipath diversity is the capturing of multipath signals into independent channels. This is done by isolating multipath components separately from each other based on their differing time delays.
The receiver do not required different RF chains(an advantage compared to space diversity) and benefit most when the multipath channel is the worst.
Disadvantage is that there is significant computational complexity in the receiver.

## Slide 8: TIME DIVERSITY
Time diversity is the use of a changing channel (due to motion of the TX or RX) at different times.
For example, one might send the same data at multiple different times but this would require multiple times the transmit power, and reduce the data rate possible on one channel. This incurs additional latency(delay).

## Slide 9: 29. Diversity combining
In the previous section, we described how we might achieve M different (nearly) independent channels.
In this section, we discuss what to do with those independent signals once we get them. These are called combining methods.
We need them for space, polarization, and multipath diversity methods.
For frequency diversity, combining is done by using OFDM receiver using frequency band signals.

## Slide 10: 29.
Here are some options:
1. Scanning Combiner: Scan among the channels, changing, when the current SNR goes below the threshold.
2.Selection Combiner: Select the maximum SNR channel’s signal and use only it.
3. Equal Gain combiner: Co- phase the signals and then add them together.
4. Maximal Ratio Combiner: The optimal solution in terms of SNR -co-phase (signals are aligned in terms of time and phase) and weight(multiply) each signal by the square root of its SNR and then add them together.

## Slide 11: 30. MIMO
Multiple Input Multiple Output (MIMO) is a particular type of space and and/ or polarization diversity in which both the transmitter and the receiver may use multiple antennas.

## Slide 12: Importance of MIMO Technology
Link Capacity: higher Maximum data that can be transferred over a link.
Spectral efficiency or bandwidth efficiency: Higher Information rate that can be transmitted over a given bandwidth.
Link reliability: high degree of perfect precision, low error rate, with sufficiently low latency.

## Slide 13: Massive mimo technology
Massive multiple-input-multiple-output (MIMO) is a wireless communication technology that uses a large number of antennas at the base station and serves multiple terminals over the same time-frequency resource.
This technique can achieve higher data rates than existing communication technology, which only serves one terminal per resource. That is why Massive MIMO is considered a promising candidate for 5G.

## Slide 14
THANK YOU